## Slide 1: Object-Oriented Internet Cloud Interoperability
Mariusz Postół Ph. D. (mariusz.postol@p.lodz.pl)
Piotr Szymczak
Institute of Information Technology, Lodz University of Technology
Notes: My name is Mariusz Postół and I am representing the Institute of the Information Technology Lodz University of Technology. It is my pleasure to present my and Piotr Szymczak research work related to Object-Oriented Internet and Cloud services integration focusing on the generic architecture that is proposed to implement and deploy this interoperability scenario.

## Slide 2: Industrial highly distributed applications - human role
Human-centric
  information origin or ultimate information destination is an operator
  GUI Based Human Interface
  Robustness (errors tolerance) depends on human interaction
  Cloud-base IoT front-end
Machine-centric
  information creation, consumption, networking, and processing are achieved entirely without human interaction
  No human interaction possible to improve solution robustness
  Cyber-physical systems based on Machine to Machine communication
  OPC Unified Architecture to promote a multi-vendor environment
Notes: Based on the role humans take while deploying the smart factory concept the computer applications may be grouped as Human-centric or Machine-centric.
A typical human-centric approach is a web service supporting a web user interface (UI) to monitor conditions and manage millions of devices and their data in a typical cloud-based Internet of Things approach. In this case, it is characteristic that any necessity to decide can be relaxed by human interaction.
An example of a machine-centric scenario is the coordination of robot behavior in a work cell. In this case, any human interaction must be recognized as impractical or even impossible. This interconnection scenario requires machine-to-machine communication (M2M) demanding multi-vendor device integration. In this case, the solution must be robust by design because no human interaction is applicable at run-time.
To promote multi-vendor environment the standardization is especially important. Industry 4.0 is an idea that addresses the Smart factory concept design and deployment. That concept is recognized as the fourth industrial revolution. Additionally, to address interoperability of the multi-vendor parts requirements the OPC Unified Architecture is considered to normalize machine to machine communication.
The main goal of this article is to prove that the cyber-physical network can be interconnected with the Internet of Things cloud services based on the OPC UA standard implemented as a powerful standalone library without dependency on the Client/Server session-oriented archetype. In the proposal, cloud interoperability can be implemented as an independent part employing out-of-band communication without dependency on the OPC UA implementation. Additionally, the proposed generic architecture allows that the gateway functionality is implemented as a composable part at run-time - no programming is required.

## Slide 3: GUI Front-end As a service
PROGRAM
Presentation
Logic
Data
Files
Database
GUI
OSI Model
Application (HTTP)
Presentation
Session
Transport (TCP)
Network (IP)
Data Link
Physical
Telemetry
HTTP Client
SERVICE

## Slide 4: Telemetry => Cyber-physical Systems
Integrated machines interconnected over the Internet
Internet of Things (IoT)
Data holder mobility:
  Mobile Device -Network attachment point
  Mobile Application - Serverless data access – reactive communication
  Mobile Data- Random location of data publication
Real-time processing
Notes: Going beyond the smart factory realm, a similar concept may be used to make any general-purpose entities interoperable. Finally, we get cyber-physical systems where a variety of entities may be aggregated into distributed information processing solutions. In this case, we are opening the public connectivity domain, which requires a globally scoped infrastructure, i.e. the Internet.
For any generic solution addressing the design of the cyber physical system, the data holder mobility must be considered as well. Mobile data means that it may come from mobile devices or be generated in unpredictable attachment points. If the data place exposition is arbitrary it means that the data appearance must be recognized and processed as an event. A good example of this scenario is a product - for example, drugs - global tracking system - an application domain where the IoT term has been coined. One of the arguments for the IoT is allowing distributed yet interlinked devices, machines, and objects (data holders) to interact with each other without relying on human interaction to set up and commission the embedded intelligence.
In this kind of application, time must be considered as an important contributor to the implemented algorithm.
In case any kind of mobility has to be considered, the next engineering challenge is dynamic discoverability on the network and the possibility of establishing the semantic and security contexts of the parts composing the IoT application.

## Slide 5: Direct Interconnection Interoperability Scenario
Notes: To promote reusability the research must be conducted atop of a formal description. The proposed solution and all intermediate steps illustrating how to derive the final solution from the selected domain features are described using the UML. Finally, the workout is abstract enough to be reused in any development environment.
On the other hand, we published two open-source implementations as proof of concept.
Before conducting any further research, we must address the question about the relationship between the cloud-based frond-end and cyber-physical network, and the first natural option is direct interconnection. By design, the direct interconnection approach requires that the cloud has to be compliant with the interoperability standard the cyber-physical system is based on.
This approach is not practical, became by design, the cloud-based services require that for interconnection preparation and data interchange is conducted over the Internet. Contrary to this, machine-to-machine communication is usually constrained by real-time requirements to use protocols applicable only to local computer networks (for example multicast IP, Ethernet, TSN, etc.).
Concluding, it is obvious that because the cloud services support only communication over the Internet the direct interconnection cannot be applied in a general case.

## Slide 6: Edge Interoperability Scenario
Notes: An edge entity is a remote cloud agent acting as an intermediary for nodes of the cyber-physical system. It is a consistent part of cloud-based frond-end services. The main disadvantage of this solution is the possibility to support interconnection with only one cloud service.

## Slide 7: Field Level Gateway Interoperability Scenario
Notes: Field level gateway is a dedicated custom agent acting as an intermediary for nodes connected to the cyber-physical network. This solution is not constrained by the cloud vendor communication context and as the result may be used to handle communication with a variety of clouds. Still, this solution is constrained to fulfill the gateway functionality only.

## Slide 8: Embedded Gateway Interoperability Scenario
Notes: To promote reusability the research must be conducted atop of a formal description. The proposed solution and all intermediate steps illustrating how to derive the final solution from the selected domain features are described using the UML. Finally, the workout is abstract enough to be reused in any development environment.
We propose a new architecture derived from the field-level approach but not constrained to gateway functionality only. The embedded gateway is only a composed part of the Networking services of a cyber-physical node. In this approach, it may be assumed that the gateway functionality is only an add-in to expand the typical functionality of the node including but not limited to establishing semantic and security context with the other nodes connected to the cyber-physical network. The responsibility of the Embedded Gateway is to establish communication context with the cloud-based frond-end and conduct the selected data transfer in compliance with the context.
Embedded Gateway is composable to any Cyber-physical node. It is worth stressing that it could be deployed far after designing and deploring the hosting cyber-physical node. The only requirement that constrains this approach is a common abstract contract usually expressed as an interface that the embedded gateway must be compliant with to be aggregated to the whole. In other words, in the proposed solution, the gateway is loosely coupled with the node contrary to the edge and field-level approaches where the gateway functionality is tightly coupled (say embedded) with the host. It improves flexibility, reusability, and in general maintenance cost.

## Slide 9: Implemenation – proof of concept
To promote and leverage
  Reusability – using the same part in many scenarios
  Flexibility - Deployment without programming
The following design patterns are applied
  Separation of concerns
  Dependency injection
  Adaptive Programming
To promote Interoperability in the multi-vendor environment the proposed proof of concept is compliant with the OPC UA Part 14 PubSub
Notes: It is a theory abstracting a generic solution meeting community expectations. In other words, it is just a set of assumptions that now we can use to propose a concrete implementation meeting the assumption. I believe that a detailed description of the implementation is not relevant to us in contrast to an analysis of how to use the proposed domain model to make strategic design decisions and functionality distribution.
- From the above discussion we can learn that the main design decisions must concern reusability (it means using the same part in many scenarios), flexibility, interoperability in the multi-vendor environment, and deployment without programming.
To meet the project requirements the following design patterns have been used
- Separation of concerns - to allow independent development of the parts.
- Dependency injection - to allow late binding of independently implemented parts.
- Adaptive Programming is used at the development and deployment stage to improve the adaptability of the program against changes in the production environment.
Piece-by-piece integration of a cyber-physical system using multi-vendor products requires that machine-to-machine communication employs international standards as the interoperability foundation. Following the presented conclusions, OPC Unified Architecture Part 14 PubSub is selected in this respect.
- By design, this standard should support the required publisher-subscriber communication pattern, but it covers only partially the requirements of the applications concerned. Therefore, our proposals shall be recognized as far beyond the specification scope, although they are still compliant with the standard.

## Slide 10: Proof of concept (pilot projects)
Notes: As I stressed previously, the proposal is backed by proof of concept reference implementations. Prototyping addresses Microsoft Azure cloud services as an example. The outcome has been just published on GitHub as the open-source repository. The proposed solutions have been harmonized with the more general concept called the Object-Oriented Internet.

## Slide 11: Sessionless (Reactive) vs Session Oriented (Interactive)
Notes: We believe or even claim that the proposed architecture can be applied to any type of cyber-physical network. This diagram presents possible options but the detailed description you can find in the independent publication. Just simplifying, we must select between interactive (based on the client-server relationship) and reactive (based on the publisher-subscriber relationship) applications archetypes. Both must be recognized as not compliant environments therefore to conduct any prototyping we must select one of them. We selected reactive interoperability (yellow box) based on the OPC Unified Architecture PubSub international standard that relaxes problems related to the real-time multi-vendor environment, network traffic asymmetry, and data holder mobility.

## Slide 12: Observation
Only reactive interoperability can be used to address:
  network traffic asymmetry
    limits of the network traffic propagation for the security reasons, for example, enforced by a firewall
  data holder mobility –
    due to data origin mobility the network node may need to move from one attachment point to another losing its previous endpoint address
Notes: This discussion can be concluded that only reactive interoperability can be used to overcome network traffic asymmetry and data holder mobility. Therefore the further work is concentrated on this communication scenario. Still, reusability of the existing concepts and solutions must be concerned.

## Slide 13: Reactive interoperability implementation
Notes: To start prototyping we did use a library called UAOOI.Networking.SemanticData - networking for short. This library offers a generic implementation of the mentioned OPC Unified Architecture PubSub standard. It is generic because allows selecting one of the transport protocols allowed by the spec to connect the node to other nodes attached to the common cyber-physical network. Additionally, using a different implementation of the Encoding component many variants of the NetworkMessage compliant with the spec are configurable and may be aggregated by the library at run-time. Encoding and underling protocol stack are responsible to support in-band machine-to-machine communication. Concluding, these composable parts are responsible to handle cyber-physical network communication.
In the proposed solution process data binding is offered by the DataRepository, which implements the IBindingFactory interface. The Producer and Consumer roles are derived from it to support bidirectional data exchange with the underlying real process. By design, they support access to real-time process data. Independent implementations of these roles can be composed by the Reactive Application using the dependency injection programming technique. It follows the separation of concerns programming concept.

## Slide 14: Implementation Domain Model
Notes: According to this diagram, our implementation of the Consumer role has been used to provide embedded gateway functionality and out-of-band communication with cloud services to transfer data to Azure IoT Central solution.
The most important feature here is that the Reactive application uses late binding to compose the custom implementation of the gateway. As I said previously it allows implementation of this role even after deploying the hosting application. In other words, current Consumer implementation is injected part of the Reactive Application compliant with the OPC UA PubSub. Using other implementations of the Producer/Consumer roles means that a vast variety of functionality can be provided at the same time.
Using many Consumer roles it is possible to get connected to any cloud services using out-of-band communication compliant with cloud services connectivity requirements. Our prototyping addresses only Azure interoperability as just an example.
It is worth stressing that the hosting application of the embedded gateway part based on the Consumer functionality is a fully functional member of the Cyber-physical Network.

## Slide 15: Implementation Architecture
PartBindingFactory: IDTOProvide
  establish semantic context
    data grouping
    data mapping
    data serialization (JSON)
  factoring Data Transfer Object
CommunicationContext based on state machine
  protocol selection
  send Data Transfer Object to Cloud
  security context
Out-of-band communictation
Notes: The implementation contains two major components, namely CommunicationContext and PartBindingFactory.
PartBindingFactory is responsible for grouping and processing the data recovered from the messages exchanged over the network. Integrating these two different environments we must assume that metadata used to describe the data exchanged over the cyber-physical networks and the data exposed by the cloud solution are not compliant.
- For example, to be compliant with the specification the cyber-physical data exchange must be described using encoding required by the OPC Unified Architecture spec. On the other hand, the cloud solution metadata may be described using Digital Tween Description Language that is not stable. In other words, these two environments use different domain-specific languages to describe the syntax and semantics of the same process data. Therefore, based on the bitstreams meaning this class of the gateway must be also responsible to provide mapping at run time. The result of the mapping is converted to Data Transfer Object using JSON serialization. This Data Transfer Object factoring mechanism must be conducted every time new data is to be sent to the cloud, but behavior implementation of the mapping may be considered as the design-time activity in a typical case.
CommunicationContext class sends the created Data Transfer Objects using a communication channel established in advance. The Data Transfer Object is retrieved from the PartBindingFactory using the IDTOProvider interface.
The CommunicationContext maintains the data transfer channel with the cloud services using a well-known state machine pattern. It is responsible for protocol stack selection, authentication, and authorization of a session created to establish a communication channel. The encoded JSON messages must be transferred to the cloud over the network using the selected protocol stack.
Azure and PubSub use different security mechanisms so in the proposed solution establishing security context is realized independently using the configuration. The CommunicationContext is responsible for establishing the connectivity and security contexts.
Finally, CommunicationContext uses out-of-band communication to send data to the cloud services.

## Slide 16: Future research
OPC UA Server Embedded Gateway
OPC UA Client Emended Gateway
Semantic mapping
Gateway on a stick
  self contained application without Cyber-physical Network interoperability
Notes: My point is that this gateway experience may be easily ported to implement OPC UA Server and OPC UA Client gateway. A next topic that could be a good candidate for further work is a systematic approach to the semantic mapping between different domain-specific languages, namely languages defined by the OPC UA specification and Digital Tween Description Language that is to be used to define metadata on the Azure services.
Additionally, a gateway on the stick should be concerned, namely self-contained application without cyber physical Network interoperability. In this case, data gathered by the producer is sent directly to the cloud using the Consumer role implemented to fulfill the gateway functionality.

## Slide 17
Thank you
Notes: That's all for now, thank you very much for your attention. We can open the Q/A session for my time slot.